## Slide 1: Safety Evening 31 May 2025 Raising Safety Awareness Safety Officer John Thomson

## Slide 2: How Safety Aware Are You?
The following slides contain 20 safety-related questions.
How many will you get correct?
Will anyone get 100% correct?
Keep your own score - it will not be publicised!

## Slide 3
How much of your scan should be outside of the cockpit when you are in the circuit?
a) 50%
b) 75%
c) 85%
d) 100%

## Slide 4
How much of your scan should be outside of the cockpit when you are in the circuit?
a) 50%
b) 75%
c) 85%
d) 100%
The BGA Collision Avoidance advice in 2024 was: lookout for at least 80% of the time

## Slide 5
You hear a powered aircraft broadcast that they are about to join for landing at Easterton on the dead side, what does the dead side mean?
a) The downwind side of the runway
b) The opposite side of the runway to where the circuit is to be flown
c) The side nearest the local cemetery
d) The aircraft will be making a power off approach

## Slide 6
You hear a powered aircraft broadcast that they are about to join for landing at Easterton on the dead side, what does the dead side mean?
a) The downwind side of the runway
b) The opposite side of the runway to where the circuit is to be flown
c) The side nearest the local cemetery
d) The aircraft will be making a power off approach
But…What side of the runway will the power pilot make their circuit? At Easterton it is usually to the North but circumstances may mean that this changes.

## Slide 7
Why might FLARM give an erroneous direction warning while flying in wave?
a) The cold experienced in high wave flights will affect FLARM performance
b) There is electrical interference from the stratosphere
c) FLARM is only certified for flight at lower levels
d) FLARM uses the ground track to determine glider heading

## Slide 8
Why might FLARM give an erroneous direction warning while flying in wave?
a) The cold experienced in high wave flights will affect FLARM performance
b) There is electrical interference from the stratosphere
c) FLARM is only certified for flight at lower levels
d) FLARM uses the ground track to determine glider heading
If the wind is strong then the aircraft will require a large heading offset to prevent being drifted back by the wind.

## Slide 9
Which of these represent the rolling recency requirements to maintain the validity of a SPL?
a) Within the last 2 years: 5 hours; 15 launches; and two training flights with an FI(S)
b) Within the last 12 months: 5 launches and 5 hours
c) Within the last 18 months: 5 hours and at least 1 training flight with an FI(S)
d) Within the last 12 months: 5 hours; 5 launches; and at least 1 training flight with an FI(S)

## Slide 10
Which of these represent the rolling recency requirements to maintain the validity of a SPL?
a) Within the last 2 years: 5 hours; 15 launches; and two training flights with an FI(S)
b) Within the last 12 months: 5 launches and 5 hours
c) Within the last 18 months: 5 hours and at least 1 training flight with an FI(S)
d) Within the last 12 months: 5 hours; 5 launches; and at least 1 training flight with an FI(S)
See regulation SFCL.160 gives full details

## Slide 11
In TEM, the T stands for which of the following?
a) Timing, this refers to the importance of timely action
b) Threats, these are external factors that have the potential to compromise flight safety
c) Threats, these are actions or decisions that deviate from intended plans or procedures
d) Timing, this refers to the requirement to only fly during daylight hours

## Slide 12
In TEM, the T stands for which of the following?
a) Timing, this refers to the importance of timely action
b) Threats, these are external factors that have the potential to compromise flight safety
c) Threats, these are actions or decisions that deviate from intended plans or procedures
d) Timing, this refers to the requirement to only fly during daylight hours
TEM – Threat and Error Management is a crucial concept that empowers pilots to identify, assess, and mitigate potential risks before they escalate into hazardous situations.

## Slide 13
What is the minimum altitude, above which an average person may experience some symptoms of hypoxia?
a) 10,000 feet
b) 15,000 feet
c) 5,000 feet
d) 18,000 feet

## Slide 14
What is the minimum altitude, above which an average person may experience some symptoms of hypoxia?
a) 10,000 feet
b) 15,000 feet
c) 5,000 feet
d) 18,000 feet
From the CAA Safety Sense Document on Mountain Flying Safety: Above 5,000 ft you may experience some loss of mental capacity and degradation of eyesight.

## Slide 15
You are flying at 50kt in a medium turn (35o) when you meet 6kt sink. How much height will you lose if you complete a full turn in the sink?
a) 120 feet
b) 180 feet
c) 240 feet
d) 300 feet

## Slide 16
You are flying at 50kt in a medium turn (35o) when you meet 6kt sink. How much height will you lose if you complete a full turn in the sink?
a) 120 feet
b) 180 feet
c) 240 feet
d) 300 feet
A 360o turn at 35o of bank and at 50kt will take 24 seconds. 24 seconds at 600fpm = 240 feet

## Slide 17
You are flying on a ridge in thermic conditions, why should you avoid flying at minimum sink?
a) You are close to the stall
b) Control authority is reduced
c) Both of the above
d) None of the above

## Slide 18
You are flying on a ridge in thermic conditions, why should you avoid flying at minimum sink?
a) You are close to the stall
b) Control authority is reduced
c) Both of the above
d) None of the above
A strong updraft may push the wing past its stalling angle. A strong thermal rising under 1 wing may bank the glider even if full control deflection is applied.

## Slide 19
You are returning to the site from far downwind on a strong wind day. Which speed will likely provide the best chance of making it back?
a) Minimum sink
b) Minimum sink + ½ the wind speed
c) Best glide
d) Best glide + ½ the wind speed

## Slide 20
You are returning to the site from far downwind on a strong wind day. Which speed will likely provide the best chance of making it back?
a) Minimum sink
b) Minimum sink + ½ the wind speed
c) Best glide
d) Best glide + ½ the wind speed
The wind is reducing your glide angle relative to the ground and extra speed is needed to compensate for this.

## Slide 21
You are returning to the site from far upwind on a strong wind day. Which speed will likely provide the best chance of making it back?
a) Minimum sink
b) Minimum sink + ½ the wind speed
c) Best glide
d) Best glide + ½ the wind speed

## Slide 22
You are returning to the site from far upwind on a strong wind day. Which speed will likely provide the best chance of making it back?
a) Minimum sink
b) Minimum sink + ½ the wind speed
c) Best glide
d) Best glide + ½ the wind speed
The wind is contributing to your speed over the ground, flying at minimum sink maximises the time that the wind has to help you.

## Slide 23
Which of these is NOT one the components of the “6S” mnemonic for field selection, if looking to land out?
a) Stock
b) Surface Wind
c) Surroundings
d) Situational Awareness

## Slide 24
Which of these is NOT one the components of the “6S” mnemonic for field selection, if looking to land out?
a) Stock
b) Surface Wind
c) Surroundings
d) Situational Awareness
Size, Slope, Surface, Stock, Surface Winds, Surroundings

## Slide 25
When flying, how close you can approach any person, vessel, vehicle or structure (excluding when taking off or landing)?
a) 100 feet
b) 200 feet
c) 500 feet
d) 1,000 feet

## Slide 26
When flying, how close you can approach any person, vessel, vehicle or structure (excluding when taking off or landing)?
a) 100 feet
b) 200 feet
c) 500 feet
d) 1,000 feet
There are UK exemptions to this which apply to gliders when hill soaring or to tugs picking up or dropping off towing apparatus at an aerodrome.

## Slide 27
Which of the following are NOT effects of operating with an under inflated main wheel?
a) The wheel’s ability to absorb landing shocks will be reduced
b) The inner tube and/or valve may be damaged
c) The ground run on take off will be longer
d) The ground run on landing will be longer

## Slide 28
Which of the following are NOT effects of operating with an under inflated main wheel tyre?
a) The wheel’s ability to absorb landing shocks will be reduced
b) The inner tube and/or valve may be damaged
c) The ground run on take off will be longer
d) The ground run on landing will be longer
The soft tyre will increase the rolling resistance of the wheel and so shorten the ground run when landing.

## Slide 29
What is the purpose of the yellow bug on a glider ASI?
a) It shows the best glide speed for no wind at maximum weight without water ballast
b) It shows the minimum sink speed at maximum weight without water ballast
c) It shows the minimum approach speed for no wind at maximum weight without water ballast
d) It shows the maximum speed to fly in rough air when carrying water ballast

## Slide 30
What is the purpose of the yellow bug on a glider ASI?
a) It shows the best glide speed for no wind at maximum weight without water ballast
b) It shows the minimum sink speed at maximum weight without water ballast
c) It shows the minimum approach speed for no wind at maximum weight without water ballast
d) It shows the maximum speed to fly in rough air when carrying water ballast

## Slide 31
Which of the following is NOT part of the HASSLL check?
a) Height
b) Location
c) Straps
d) Speed

## Slide 32
Which of the following is NOT part of the HASSLL check?
a) Height
b) Location
c) Straps
d) Speed
From the BGA Instructor Manual, Checklists:
Height; Airframe; Straps; Security; Location; Lookout.

## Slide 33
You are pulling out of a steep dive but you are approaching both Vne and the g limit for the aircraft. Do you?
a) Pull harder to avoid over-speeding
b) Open the airbrakes to avoid over-speeding
c) Reduce the back pressure on the stick to avoid too much g
d) Enter a sideslip to avoid over-speeding

## Slide 34
You are pulling out of a steep dive but you are approaching both Vne and the g limit for the aircraft. Do you?
a) Pull harder to avoid over-speeding
b) Open the airbrakes to avoid over-speeding
c) Reduce the back pressure on the stick to avoid too much g
d) Enter a sideslip to avoid over-speeding
G is an elastic limit; Airbrakes reduce the G limit for the airframe;
Flutter and airframe disintegration will occur at not much over Vne;
A sideslip near Vne will overstress the tail of the aircraft.

## Slide 35
Below Va a sailplane must be able to withstand:
a) All controls simultaneously moved to full deflection
b) Any one control moved to full deflection
c) A 5g pull out from a dive
d) Turns of up to 60o

## Slide 36
Below Va a sailplane must be able to withstand:
a) All controls simultaneously moved to full deflection
b) Any one control moved to full deflection
c) A 5g pull out from a dive
d) Turns of up to 60o
BGA Theory of Flight For Glider Pilots

## Slide 37
A glider has a Vne of 150kt. What is the fastest speed that the manufacturer must test fly the aircraft to?
a) 150kt
b) 159kt
c) 178kt
d) 195kt

## Slide 38
A glider has a Vne of 150kt. What is the fastest speed that the manufacturer must test fly the aircraft to?
a) 150kt
b) 159kt
c) 178kt
d) 195kt
Vd = 167kt, Vne = 0.9x Vd = 150kt, Vdf = 0.95xVd = 159kt
NB the 159kt was flown in a brand new aircraft in ideal conditions by a specially trained test pilot…

## Slide 39
A “Pan Pan” call on the aircraft radio means:
a) Urgent help is required
b) Immediate help is required
c) Help may be required
d) Help is no longer required

## Slide 40
A “Pan Pan” call on the aircraft radio means:
a) Urgent help is required
b) Immediate help is required
c) Help may be required
d) Help is no longer required
As per ICAO terminology, Rules of the Air,
Annex 2, Appendix 1

## Slide 41
You are manning the launch point radio. A power pilot
(G-ABCD) calls to ask if the runway is clear (which it is).
Which of the following is the best response?
a) All Clear
b) G-ABCD, Easterton Ground, Confirm
c) G-ABCD, Easterton Ground, Affirmative
d) G-ABCD, Go Ahead

## Slide 42
You are manning the launch point radio. A power pilot
(G-ABCD) calls to ask if the runway is clear (which it is).
Which of the following is the best response?
a) All Clear
b) G-ABCD, Easterton Ground, Confirm
c) G-ABCD, Easterton Ground, Affirm
d) G-ABCD, Go Ahead
a) and d) are ambiguous, b) may be interpreted as repeat your message, c) is the best answer

## Slide 43
Have fun, fly safe!
The End!